## Slide 1: Understanding your electricity bill
David Neyle
Volunteer Community Energy Coordinator

## Slide 2: Reading your electricity bill
It can appear quite confusing!
Important to understand what you are paying for so you can manage it

## Slide 3: Objectives for today
Explain the difference between ‘power’ and ‘energy’
Identify big energy using appliances in the home
Locate your NMI number
Identify the different tariffs and tariff pricing on your electricity bill
Analyse the total cost of your electricity bill and compare to community averages
Assess and consider practical actions you could take to reduce your electricity bill

## Slide 4: “Power” and “Energy”

## Slide 5: “Power” and “Energy”

## Slide 6: “Power”
Power is the instantaneous amount of electricity being used
Measured in ‘Watts’ (W) [a thousand Watts is a kilowatt, kW]
Electrical appliances are rated in Watts or kilo Watts (kW) – the bigger the number the more power required to make them work.

## Slide 7: “Energy”
Energy is Power x Time
Electrical energy is measured in watt.hours (Wh)
A thousand watts of electric power used over an hour is 1 kilowatt.hour (kWh)

## Slide 8: “Energy”
Two appliances with the same power rating – 2kW
Electric kettle, 2kW, takes a minute to boil
  2kW x 40c/kWh x 1/60 = 1.3 cents
  Bar radiator, 2000W (2kW) used for 2 hours = 4kWh
  2kW x 40c/kWh x 2 hours, therefore $1.60 to run for 2 hours

## Slide 9: “Electrical Energy”
The amount of electricity (energy) you use and get charged $$ for =
  Rating of the appliance
  How long it is consuming electricity
  Shows on your bill as kWh

## Slide 10: Big electricity energy appliances

## Slide 11: Big electricity energy appliances
Pool pump
2.4kW x 3 hours = 7.2kWh

## Slide 12: Big electricity energy appliances
Resistive Element Hot Water Service
3kW x 4 hours = 12kWh

## Slide 13: Big electricity energy appliances
Heating-element Clothes Dryer
2.4kW x 2 hours = 4.8kWh
~ $1.92

## Slide 14: Big electricity energy appliances
Fan Heater ($19)
2kW x 6 hours = 12kWh
In three rooms?
12kWh x 3 = 36kWh = $14.40
Over 90 days = $1,296

## Slide 15: Big electricity energy appliances
Modern refrigerator
About 1kWh – 2kWh per day

## Slide 16: ‘Zombie’ appliances
Appliances that continue to draw electricity when powered down (STANDBY MODE)
Very small overall impact on your bill
Notes: ‘Standby’ power consumption. Not the problem it was in the past. New appliances must have minimal standby energy consumption. Probably more dangerous and difficult trying to get down to the power point to turn them on and off.

## Slide 17: Supply charge
Fixed amount, regardless of how much electricity you use
Pays for “poles and wires” – electricity distribution and administration costs
Currently about $2.00/day
  $2.00 x 365 = ~ $720 year
If you have ‘off-peak’ hot water (controlled load), then about 20c/day is included in your supply charge. If you don’t have OPHW then your supply charge will be about 20c/day cheaper
Can’t be avoided unless you disconnect from the electricity grid.

## Slide 18: Tariffs
What you pay per kWh – usage
There are a range of tariffs that you may or may not be using.
Fixed tariff – most common
  ~ 40c/kWh
  Applies all day (24h /7 days week)
Controlled Load
  ~ 20c/kWh (OP hot water)
  Supply is disconnected during peak periods
  You are given the discounted tariff to compensate for not having electricity available during peak periods
These types of tariffs have been around for many years and are what people are most accustomed to seeing on their bill.

## Slide 19: Tariffs
Time of use tariffs
A more recent innovation to encourage users to manage their use of electricity to assist the generators and distributors to manage the network.
Introduces three new tariffs:
  Peak ~ 45c / kWh
  Shoulder ~ 40c / kWh
  Off-peak (different to OP hot water tariff) ~ 30c / kWh
Could be advantageous if you really focus on managing when you use electricity
Most people are being transferred to these plans, which might end up costing you more!

## Slide 20: Time of Use – Essential Energy

## Slide 21: Feed-In Tariff
What you are paid for selling your generated electricity back to the retailer
Usually, excess solar electricity
Very low = ~5c kWh
  5kW x 8 hours x $0.05 = $2/day (at best!)

## Slide 22
National Meter Identifier (NMI)

## Slide 23: What is the meter/register reading?
Smart Meter
Analogue Meter

## Slide 24: Meters in your Meterboard
They ‘register’ your electricity usage and network feed-in
Smart meters are able to be read remotely
Old analogue meters require a meter reader
  You may get an ‘estimate’ read
Smart meters may have more than one register, especially if you have 3-phase power to the property
Shows on your bill as a meter or register reading
  ‘start’ and ‘finish’ number for the period of the bill

## Slide 26
‘B’ register = solar feed in
‘E1’ register = General use
‘E2’ register = Controlled load

## Slide 27: Analyse your bill
How much electricity am I using compared to an average user?
  Average house 15kWh  20kWh per day

## Slide 28: Group Exercise
Find your NMI number on your bill
Your contract: Fixed rate tariff or Time-of-use tariff?
What is your daily supply rate cost?
What are the various tariff rates you are paying?
How many days/period is your bill for?
Based on your daily usage, does it seem about right or not?
Given what you have learnt about energy consumption and tariff rates, in order to reduce your bill, what is one thing you could consider doing?

## Slide 29: Don’t pay the ‘lazy tax’
Shop around regularly!
Ask for a better deal (they keep them under the counter!)
https://www.energymadeeasy.gov.au/